The V5 integrator for electric guitar pickup measurements can be divided into four functional blocks. Each one is actually performed by one op amp. One, IC1D, supplies the approximately half supply voltage to provide a reference voltage for bipolar operation from a single voltage supply. Zener D1 reverse voltage of 5.1V is filtered by a capacitor and supplied to the input of the amp, which is configured as a voltage follower.

IC1C is a preamplifier for the signal from the pickup under test. A switch allows a choice of 0dB or 6dB gain. The test input first feeds a high impedance network that provides isolation from the preamplifier input circuit. It is almost identical to the circuit in a typical oscilloscope probe. However, it can have lower capacitance because a long cable is not required and so does not need to be compensated. As with the scope probe, there is a variable cap that can be used to calibrate the network. The network input has an approximately 11M ohm resistance and 10pF capacitance. A three-way switch allows the input to be loaded by a standard RC test load, an inductance test load, or no load.

IC1B is an analog integrator with a very low frequency cutoff to provide op amp DC stability. The blocking capacitor C5 is needed to eliminate the DC input sensitivity caused by the large value of R6.

IC1A is a post amplifier and output line driver.